## Slide 1: Lecture 5 &Lecture6
Introduction Of Wireless Lan Network

## Slide 2: Introduction
A wireless LAN (WLAN) is a wireless computer network that links two or more devices using wireless communication to form a local area network (LAN) within a limited area.
Most modern WLANs are based on IEEE 802.11 standards and are marketed under the Wi-Fi brand name(Wi-Fi).
The Wi-Fi Alliance is a non-profit organization that owns the Wi-Fi trademark
IEEE 802.11 supports two modes of network topology: infrastructure and ad hoc, also called independent (IBSS) mode., all 802.11 transceivers are in the direct range of an access point. In infrastructure mode at handles all nodes within its range.
Fig 1 WLAN Architecture

## Slide 3: Cont ..
In ad hoc mode, 802.11 transceivers can communicate directly with each other, without the need for an access point in range. Although most 802.11 transceivers support the ad hoc mode or Independent BSS (also referred to as IBSS), infrastructure mode is mostly used.
Every 802.11 transceiver is associated with one of the access points. Communication between nodes goes through the access points or directly over the radio medium. If nodes are in range of each other, they directly communicate with each other.
Otherwise, they communicate by sending their packets to the access point to which they are associated. Communication with outside networks always goes through the access point.

## Slide 4
IEEE 802.11 standard | Year | Max data rate | Range | Frequency
802.11b | 1999 | 11 Mbps | 30 m | 2.4 Ghz
802.11g | 2003 | 54 Mbps | 30m | 2.4 Ghz
802.11n (WiFi 4) | 2009 | 600 | 70m | 2.4, 5 Ghz
802.11ac (WiFi 5) | 2013 | 3.47Gpbs | 70m | 5 Ghz
802.11ax (WiFi 6) | 2020 (exp.) | 14 Gbps | 70m | 2.4, 5 Ghz
802.11af | 2014 | 35 – 560 Mbps | 1 Km | unused TV bands (54-790 MHz)
802.11ah | 2017 | 347Mbps | 1 Km | 900 Mhz
all use CSMA/CA for multiple access, and have base-station and ad-hoc network versions
Physical Layer
The following table are describe the specifications that employ in 802.11 physical layer with data rate .

## Slide 5: Elements of a wireless LAN network
network
infrastructure
wireless hosts
laptop, PDA, IP phone
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility
Fig2 Elements of a wireless LAN network

## Slide 6: Station Types
Station with no-transition mobility is either stationary (not moving) or moving only inside a BSS.
Station with BSS-transition mobility can move from one BSS to another, but the movement is confined inside one ESS.
A station with ESS-transition mobility can move from one ESS to another.
IEEE 802.11 does not guarantee that communication is continuous
during the move.

## Slide 7: Cont..
network
infrastructure
base station
typically connected to wired network
AP are similar to bridges, but connect many wireless users devices (NICs) to one
network (e.g. Ethernet) and forward all frames received (no filtering).
It responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points
Fig3. Elements of a wireless LAN network

## Slide 8: Cont..
network
infrastructure
wireless link
typically used to connect mobile(s) to base station
also used as backbone link
multiple access protocol coordinates link access
various data rates, transmission distance
Fig4 Elements of a wireless LAN network

## Slide 9: IEEE802.11 - Architecture of an infrastructure network
Basic Service Set
IEEE 802.11 defines the basic service set (BSS) as the building block of a wireless LAN. A basic service set is made of stationary or mobile wireless stations and an optional central base station, known as the access point (AP).
Every BSS has an identification (ID) called the BSSID, which is the MAC address of the access point servicing the BSS.
A BSS without an AP is called an ad-hoc network ; a BSS with an AP is called an infrastructure network.

## Slide 10: Cont..
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router
Fig5 Elements of a wireless LAN network

## Slide 11: Extended Service Set
An extended service set (ESS) is made up of two or more BSSs with APs. In this case, the BSSs are connected through a distribution system, which is usually a wired LAN. The distribution system connects the APs in the BSSs. IEEE 802.11 does not restrict the distribution system; it can be any IEEE LAN such as an Ethernet.

## Slide 12
Fig6 Types of wireless LAN network

## Slide 13: Distribution system
A distribution system (DS) connects access points in an extended service set. The concept of a DS can be used to increase network coverage through roaming between cells.
DS can be wired or wireless. Current wireless distribution systems are mostly based on MESH protocols, though other systems are in use.
Interconnection network to form one logical network (EES: Extended Service Set) based on several BSS.

## Slide 14: IEEE802.11 - Architecture of an infrastructure network
Fig7 Elements of a wireless LAN network

## Slide 15
Fig8 Elements of a wireless LAN network

## Slide 16: IEEE802.11 - Architecture of an ad-hoc network
Direct communication within a limited range
Station (STA):
Terminal with access mechanisms to the wireless medium.
Independent Basic Service Set(IBSS).
Group of stations using the same radio frequency.
Fig9 Elements of a wireless LAN network

## Slide 17: IEEE standard 802.11
mobile terminal
fixed terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure network
access point
LLC
LLC
Fig10 TCP/IP layer of a wireless LAN network

## Slide 18: Logical Link Control (LLC)
The functions of Logical Link Control (LLC) are:-
Flow control
Error control

## Slide 19: MAC Sub-layer
IEEE 802.11 defines two MAC sub layers:
Distributed coordination function(DCF).
Point coordination function (PCF).

## Slide 20: Distributed Coordination Function(DCF)
DCF uses CSMA/CA as the access method, the following step will describe it:
Before sending a frame, the source station senses the medium by checking the energy level at the carrier frequency.
a. The channel uses a persistence strategy with back off until the channel is idle.
b. After the station is found to be idle, the station waits for a period of time called the distributed interframe space (DIFS); then the station sends a control frame called the request to send (RTS).
IEEE 802.11: multiple access

## Slide 21
2-After receiving the RTS and waiting a period of time called the short interframe space (SIFS), the destination station sends a control frame, called the clear to send (CTS), to the source station. This control frame indicates that the destination station is ready to receive data.
3-The source station sends data after waiting an amount of time equal to SIFS.
4-The destination station, after waiting an amount of time equal to SIFS, sends an acknowledgment to show that the frame has been received. Acknowledgment is needed in this protocol because the station does not have any means to check for the successful arrival of its data at the destination.

## Slide 22: Network Allocation Vector
How do other stations defer sending their data if one station acquires access?
The key is a feature called NAV.
When a station sends an RTS frame, it includes the duration of time that it needs to occupy the channel. The stations that are affected by this transmission create a timer called a network allocation vector (NAV) that shows how much time must pass before these stations are allowed to check the channel for idleness.
Each time a station accesses the system and sends an RTS frame, other stations start their NAV. In other words, each station, before sensing the physical medium to see if it is idle, first checks, its NAV to see if it has expired. Figure 15.7 shows the idea of NAV.

## Slide 23
Fig 12 CSMA/CA and NAV

## Slide 24: Point Coordination Function (PCF)
The point coordination function (PCF) is an optional access method that can be implemented in an infrastructure network (not in an ad hoc network).
It is implemented on top of the DCF and is used mostly for time-sensitive transmission.
PCF has a centralized, contention-free polling access method.
The stations are polled one after another, sending any data they have to the AP.
To give priority to PCF over DCF, another interframe space, PIFS, has been defined.

## Slide 25
PIFS (PCF IFS) is shorter than DIFS. This means that if, at the same time, a station wants to use only DCF and an AP wants to use PCF.
Due to the priority of PCF over DCF, stations that only use DCF may not gain access to the medium.
To prevent this, a repetition interval has been designed to cover
both contention-free PCF and contention-based DCF traffic.
The repetition interval, which is repeated continuously, starts with a special control frame, called a beacon frame.
When the stations hear the beacon frame, they start their NAV for the duration of the contention-free period of the repetition interval.

## Slide 26
During the repetition interval, the PC (point controller or Access point) can send a poll frame, receive data, send an ACK, receive an ACK, or do any combination of these (802.11 uses piggybacking).
At the end of the contention-free period, the PC sends a CF end (contention-free end) frame to allow the contention-based stations to use the medium.

## Slide 27
Fig13 MAC protocols in WLAN

## Slide 28: Hidden and Exposed Station Problems
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other
means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 29: Hidden station problem
Fig 14 Hidden station problem

## Slide 30: Exposed station problem
Station A is transmitting to station B.
Station C has some data to send to station D, which can be sent without interfering with the transmission from A to B.
However, station C is exposed to transmission from A; it hears what A is sending and thus refrains from sending.
In other words, C is too conservative and wastes the capacity of the channel.

## Slide 31: Exposed station problem
Fig 15 Exposed station problem

## Slide 32: Hidden-Station Problem
The solution to the hidden station problem is the use of the handshake frames (RTS and CTS). Figure 14 also shows that the RTS message from B reaches A, but not C. However, because both B and C are within the range of A, the CTS message, which contains the duration of data transmission from B to A, reaches C. Station C knows that some hidden station is using the channel and refrains from transmitting until that duration is over.

## Slide 33: Fragmentation
The wireless environment is very noisy; a corrupt frame has to be retransmitted. The protocol, therefore, recommends fragmentation.
It is division of a large frame into smaller ones. It is more efficient to resend a small frame than a large one.

## Slide 34: 802.11 frame: addressing
2
2
6
6
6
2
6
0 - 2312
4
Address 1: MAC address of wireless host or AP to receive this frame
Address 4: used only in ad hoc mode
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 3: MAC address of router interface to which AP is attached
Fig 16 802.11 frame addressing

## Slide 35: 802.11 frame: addressing
Internet
H1
R1
AP MAC addr
address 1
address 2
address 3
802.11 WiFi frame
R1 MAC addr
H1 MAC addr
R1 MAC addr
MAC dest addr
MAC source addr
802.3 Ethernet frame
H2 MAC addr
Fig 17 802.11 frame addressing

## Slide 36: 802.11 frame: addressing
2
2
6
6
6
2
6
0 - 2312
4
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
duration of reserved
transmission time (RTS/CTS)
frame sequence # (for reliable data transfer)
2
2
4
1
1
1
1
1
1
1
1
type
from
AP
subtype
to
AP
more
frag
WEP
more
data
power
mgt
retry
rsvd
protocol
version
frame type (RTS, CTS, ACK, data)
Fig 18 802.11 frame addressing

## Slide 37: 802.11: Channels, association
spectrum divided into channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
arriving host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  then may perform authentication then typically run DHCP to get IP address in AP’s subnet
BSS
Fig 19 802.11: Channels, association

## Slide 38: 802.11: mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
H1
BSS 2
BSS 1
switch: which AP is associated with H1?
Fig 20 802.11: mobility within same subnet

## Slide 39: Association
In 802.11, each wireless station needs to associate with an AP before it can send or receive network layer data.
Associating means the wireless device creates a virtual wire between itself and the AP.
The 802.11 standard does not specify an algorithm for selecting which of the available APs to associate with it.
The 802.11 standard requires that an AP periodically send beacon frames, each of which includes the AP’s SSID and MAC address.

## Slide 40
The device chooses the AP whose beacon frame is received with the highest signal strength.
The process of scanning channels and listening for beacon frames is known as passive scanning.
A wireless device can also perform active scanning, by broadcasting a probe frame that will be received by all APs within the wireless device’s range.
APs respond to the probe request frame with a probe response frame. The wireless device can then choose the AP with which to associate from among the responding APs.

## Slide 41
After selecting the AP with which to associate, the wireless device sends an association request frame to the AP, and the AP responds with an association response frame.
Note that this second request/response handshake is needed with active scanning, since an AP responding to the initial probe request frame doesn’t know which of the (possibly many) responding APs the device will choose to associate with.

## Slide 42: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1
Fig 21 802.11: passive/active scanning

## Slide 43: Power Management
A node is able to explicitly alternate between sleep and wake states.
A node indicates to the access point that it will be going to sleep by setting the power-management bit in the header of an 802.11 frame to 1.
A timer in the node is then set to wake up the node just before the AP is scheduled to send its beacon frame.(recall that an AP typically sends a beacon frame every 100 msec).
Since the AP knows from the set power-transmission bit that the node is going to sleep, it (the AP) knows that it should not send any frames to that node, and will buffer any frames destined for the sleeping host for later transmission.

## Slide 44
A node will wake up (a wakeup time is 250 microseconds) just before the AP sends a beacon frame, and quickly enter the fully active state.
The beacon frames sent out by the AP contain a list of nodes whose frames have been buffered at the AP.
If There are no buffered frames for the node, it can go back to sleep. Otherwise, the node can explicitly request that the buffered frames be sent by sending a polling message to the AP.
A node that has no frames to send or receive can be asleep 99% of the time, resulting in a significant energy savings.

## Slide 45: 802.11: advanced capabilities
Rate adaptation
base station, mobile dynamically change transmission rate (physical layer modulation technique) as mobile moves, SNR varies
10
20
30
40
SNR(dB)
BER
10-1
10-2
10-3
10-5
10-6
10-7
10-4
QAM256 (8 Mbps)
QAM16 (4 Mbps)
BPSK (1 Mbps)
operating point
1. SNR decreases, BER increase as node moves away from base station
2. When BER becomes too high, switch to lower transmission rate but with lower BER
Fig 22 802.11: Rate adaptation